## Slide 1: Introduction to Computational Thermodynamics
Section 3.1
Pressure and Volume Solvers

## Slide 2: Introduction
Part 1 showed some fundamentals. Primarily, we discussed
  Automatic differentiation
  Newton’s method

## Slide 3: Introduction
Part 1 showed some fundamentals. Primarily, we discussed
  Automatic differentiation
  Newton’s method
In Part 2 you saw a broad overview of the different equations of state (EoS) available

## Slide 4: Introduction
Part 1 showed some fundamentals. Primarily, we discussed
  Automatic differentiation
  Newton’s method
In Part 2 you saw a broad overview of the different equations of state (EoS) available
Part 3 will show how to use an EoS to obtain less-obvious properties of interest
Section 3.1 discusses solving an equation of state for the volume at a given pressure and temperature

## Slide 5: Introduction
Part 3 will show how to use an EoS to obtain less-obvious properties of interest
Section 3.1 discusses solving an equation of state for the volume at a given pressure and temperature

## Slide 6: Cubic EoS
Cubic equations of state are typically shown as having the form
Notes: So, to begin with the simplest class of equations of state capable of capturing phase equilibria: the cubics. Frequently, these are worked with in this form, [NEXT SLIDE]

## Slide 7: Cubic EoS
Cubic equations of state are typically shown as having the form
Where the values of depend on the equation of state (van der Waals, Peng Robinson, Redlich Kwong)
Notes: With values of delta_1 and delta_2 depending on the equation of state

## Slide 8: Cubic EoS
Cubic equations of state are typically shown as having the form
It is not immediately obvious why we consider these to be “cubic”
Notes: Unless you have prior experience working with these, it is not usually obvious why we consider this to be a “cubic”, or why that even matters!

## Slide 9: Cubic EoS
For simplicity, we will consider the case of van der Waals, where and
Notes: So, for the sake of clarity, let us work with the van der Waals equation of state. Here, delta is 0, and our alpha-function is just 1.

## Slide 10: Cubic EoS
For simplicity, we will consider the case of van der Waals, where and
We can then multiply through by the denominators
Notes: Once we multiply through by the denominators of each fraction, (highlight movement with pen), and tidy up a little by collecting some terms, we see the familiar shape of a cubic polynomial appear

## Slide 11: Cubic EoS
We can then multiply through by the denominators
Giving us a cubic equation we can solve for !
Notes: This can now be solved for v analytically!

## Slide 12: Cubic EoS
Often, this is defined in terms of the compressibility factor
Notes: Often, we express this polynomial in terms of the compressibility factor, where the compressibility factor is a dimensionless expression describing the deviation from ideal gas behaviour

## Slide 13: Cubic EoS
Often, this is defined in terms of the compressibility factor
Which, when substituted into our expression, yields
Notes: Which, when we substitute into our expression, we get this. Still clearly Cubic, but no longer explicit in volume.

## Slide 14: Cubic EoS
This is then simplified by defining two constants, and
Notes: Because the expression is somewhat messy, it is common to tidy this up by defining two constants, capital A and capital B.

## Slide 15: Cubic EoS
This is the form you are most likely to see in literature!
When plotted on top of the saturation curve, we see three roots
Notes: If you read any textbooks or literature about cubic equations of state, and they discuss the solving of them, this will usually be the form you see

## Slide 16: Cubic EoS
Notes: First thing to note is that when three real roots are found, the middle root is always unphysical. Then, if the point we are evaluated is saturated, the smallest volume root represents the liquid state and the largest volume root represents the vapour state.
Another important feature is the maxwell equal-area construction. Under this

## Slide 17: Cubic EoS
All cubic equations are analytically solvable
This allows us to cheaply evaluate all volume roots
When more than one real root is present, the chemical potentials are evaluated and the most stable phase is chosen

## Slide 18: Cubic EoS
Show implementation in notebook
Notes: poly = [-A*B, A, -(1+B), 1.0] # Polynomial coefficients
Zvec = roots(poly) # Solve polynomial for Z
Vvec = Zvec.*(R*T/p) # Transform to volume

## Slide 19: SAFT EoS
SAFT EoS are expressed as the residual Helmholtz free energy
To solve for volume at a specified we need a function we can then solve for the volume
As with cubic EoS, usually there is more than one root – a SAFT EoS can have up to 5!

## Slide 20: SAFT EoS
Typical case for PCSAFT:

## Slide 21: SAFT EoS
However, an alternative approach resulting in faster convergence is available
We can begin with the definition of isothermal compressibility
This can be integrated to obtain a recurrence relation in

## Slide 22: SAFT EoS
One way to obtain this expression would be to take a partial derivative of
This can then be solved using any nonlinear root-finding algorithm

## Slide 23: SAFT EoS
Which we can transform to
Interestingly, this turns out to be equivalent to the relation formed by applying the Newton method to our first derivation

## Slide 24: Initial Guesses
As we cannot cheaply solve for every root, we must control which root we converge to via the initial guess
A vapour-like initial guess can be generated from the ideal gas equation
Liquid-like guesses can be generated by considering the limit of the packing fraction

## Slide 25: Initial Guesses
The packing fraction () is defined as fraction of volume in a unit cell taken up by fluid molecules
Low
High

## Slide 26: Initial Guesses
For SAFT equations, this is calculated as
The limit as is the minimum volume our fluid can occupy

## Slide 27: Implementation
Switch to notebook to show implementation

## Slide 28: Key messages
The primary advantage of cubic EoS is how cheap they are to solve for the volume at a given pT
SAFT EoS must be solved numerically
The root converged to for SAFT EoS is controlled through the initial guess
Generally, both liquid and vapour roots should be converged to determine which is more stable

## Slide 29: Convergence
Typically this method converges quickly and reliably