## Slide 1: Introduction to Computational Thermodynamics
Section 3.3
Chemical Stability Analysis

## Slide 2: Introduction
Stability analysis deals with the question “does a phase-split occur?”
This helps us determine if a single-phase solution is correct, or if further calculation is necessary
If further calculation is required, stability analysis can provide good initial guesses

## Slide 3: The Gibbs tangent-plane
This is the fundamental description of thermodynamic stability
We know a system always exists at the minima on the Gibbs free energy surface
When a tangent plane with a lower can be constructed, we know a phase-split will occur
For a binary mixture this is quite easy to show

## Slide 4: The Gibbs tangent-plane
Any plane tangent at one point signifies instability
However, there is only one cotangent plane – this shows the resulting phase split compositions

## Slide 5: The Gibbs tangent-plane
If we look at a ternary mixture of ethane, octane, and propane it becomes far harder to see where exactly the phase split occurs

## Slide 6: Mathematical description
To implement this on a computer, we need a mathematical description of instability

## Slide 7: Mathematical description
To implement this on a computer, we need a mathematical description of instability
Following the description from Michelsen, this can be motivated by considering the Gibbs free energy () must be at a global minimum

## Slide 8: Mathematical description
To implement this on a computer, we need a mathematical description of instability
Following the description from Michelsen, this can be motivated by considering the Gibbs free energy () must be at a global minimum
The change in upon the formation of of a new phase with composition from a mixture with composition can be written as

## Slide 9: Mathematical description
For to be at a minimum, no change can reduce it. Therefore for any value of
Physically this represents the distance from the surface at to a tangent plane constructed at
We call this the tangent plane distance function,

## Slide 10: Mathematical description
Our function describing chemical stability is then

## Slide 11: Mathematical description
Another way of considering this algorithmically is
  Evaluate every minimum of
  If for every minimum found
    return STABLE
  Else
    return UNSTABLE
The issue then becomes: how do we find the minimum of ?

## Slide 12: Numerical issues
Currently, our problem is a constrained optimisation problem
Because we are using mole fractions, each iteration must satisfy
This is doable, but if we change our problem description slightly we can regain the advantage of unconstrained optimisation, and once again be able to apply the standard Newton’s method

## Slide 13: Improved formulation
Once again following the route of Michelsen, we begin by expressing this in terms of fugacity coefficients
Notes: Mu_i^* is the pure component fugacity

## Slide 14: Improved formulation
Once again following the route of Michelsen, we begin by expressing this in terms of fugacity coefficients
To improve the “scaling” of our problem, we use the standard scaling factor

## Slide 15: Unconstrained formulation
The previous form is generally easier to work with as
  The scaling is improved
  It is formulated in terms of the fugacity coefficient
However, the issue of the mass fraction constraints is still not resolved
Because of this, a new function is used Where represents the vector of mole numbers
Notes: It is important to realise that tm(X) is _not_ the same as tpd, but rather a related but new function turning out to be more convenient

## Slide 16: Unconstrained formulation
The only remaining constraint is that all mole numbers must be positive
However, an elegant solution to this exists
By moving our iterations to log-space, such that every value of is guaranteed to be positive

## Slide 17: Unconstrained formulation
This function is not equivalent to
However:
  if a point is a minima of then it is also a minima of
  A negative value of implies a negative value of
This means we can use as a substitute for

## Slide 18: Unconstrained formulation
The function can be rewritten as
As the bracketed term is always positive, a negative value of is necessarily a negative value of
Therefore, if we encounter a negative value of , we can terminate our algorithm and declare the mixture unstable

## Slide 19: Unconstrained formulation
However, a positive value of does not mean a positive value of
One way to resolve this is after locating the minima of , using the function to evaluate whether those minima imply stability or not
This method is applicable to any number of components

## Slide 20: Implementation
We will split the implementation into three stages:
  Specify state and model
  Generate initial guesses
  Minimise objective function

## Slide 21: 1. State and model specification
For a phase split to occur, we must have non-ideal mixing
To capture this, we must have a prediction for the binary interaction parameters
I have chosen the Extended Predictive Peng Robinson-78 (EPPR78)

## Slide 22: 1. State and model specification
For a phase split to occur, we must have non-ideal mixing
To capture this, we must have a prediction for the binary interaction parameters
I have chosen the Extended Predictive Peng Robinson-78 (EPPR78)
For our mixture we use methane and hydrogen sulfide evaluated at 187 K, 4.052 MPa

## Slide 23: 2. Initial guesses
For initial guesses, we use the Wilson correlation
Provides us with K-factors, defined as
Designed to match the pure component vapour pressure at and

## Slide 24: 2. Initial guesses
For initial guesses, we use the Wilson correlation
Provides us with K-factors, defined as
Designed to match the pure component vapour pressure at and
Generally performs well. Very poor predictions when used with hydrogen

## Slide 25: 3. Minimise
To minimise our objective function, Newton’s method is highly effective

## Slide 26: 3. Minimise
To minimise our objective function, Newton’s method is highly effective
Because we aim to evaluate all minima of the function we use multiple starting points

## Slide 27: 3. Minimise
To minimise our objective function, Newton’s method is highly effective
Because we aim to evaluate all minima of the function we use multiple starting points
In optimisation, this is often referred to as multi-start

## Slide 28: 3. Minimise
We choose two guesses for our initial compositions. One liquid-like and one vapour-like.
The liquid-like phase composition:
The vapour-like phase composition:

## Slide 29: 3. Minimise
Switch to notebook and show implementation
Notes: # Solve for our liquid and vapour guesses
optf = OptimizationFunction(f, Optimization.AutoForwardDiff())
prob(x0) = OptimizationProblem(optf, log.(x0))
sol(x0) = solve(prob(x0), Newton())
# Evaluate solutions
sol_vec = sol.(x0_vec)

## Slide 30: Equilibrium guesses
One of the key applications of stability analysis is providing good “guesses” of equilibrium
Notes: These are incredibly useful when applying stability analysis as the precursor to a full flash algorithm. A flash algorithm is the terminology for the calculation of the “equilibrium tangent plane”, and will be the focus of our next section

## Slide 31: Key points
When considering the Gibbs tangent plane criterion, there is only a single cotangent plane representing the equilibrium compositions
There are infinite tangent planes that can signal chemical instability
To calculate the tangent plane distance, we transform our function to an surrogate unconstrained function
Stability analysis is an important tool in its own right, as well as providing initial guesses to further calculations